From http://llvm.org/docs/LangRef.html

* identifiers: [%@][-a-zA-Z$._][-a-zA-Z$._0-9]*
* @ global identifiers
* % local identifiers

* unnamed values: %[-._0-9]* // ex) %12, @2, %44 // unnamed temporaries are numbered sequentially. Using per-function incrementing counter, starting from 0

* escape letter: \xx // with xx ASCII hexadecimal
* comments: ;[comments]

* linkage types
- private: within module
- internal: within module, local symbol (static of C)
- available_externally: outside module // allows inlining, optimization // allowed to discard this linkage at will // allowed on definitions not declaration
- linkonce: merged with other globals with same name // discarded if unreferenced // no inlining (definition is not clear within a module)
- linkonce_odr: allows inlining
- weak: semantic alike linkonce // won’t be discarded (weak of C)
- weak_odr: Only Definition Rule in such as C++, only equivalent globals merge
- common: most similar to weak // must have a zero initializer // functions and aliases don’t have common linkage (int x; of C)
- appending: for global vars & pointer to array type // appends together when linked // for special vars like llvm.global_ctors (?)
- extern_weak: weak until linked // when unlinked, becomes null instead of being undefined
- external: externally referencible

*calling conventions